## Slide 1
CYBERFORGE 2026 · IDEATION SUBMISSION · AI SECURITY
VILLE
Verified Inference Leak Locator using E-values
Detecting when a compromised AI inference server is secretly leaking its model weights — without drowning security teams in false alarms.
Team REIGN · Chittimilla Saitarun · SaiNithin Pokala
Based on arXiv:2610.11843 · github.com/Nithyon/ville

## Slide 2
01 · PROBLEM STATEMENT
A hacked inference server can steal the model it serves, hidden inside ordinary-looking answers.
— The server holds the model weights and chooses every output token.
— When two next tokens are almost equally likely, picking one or the other can encode a payload bit.
— The text still reads normally, so content filters and DLP see nothing wrong.
— A server must return tokens, so this channel can be monitored and rate-limited — but never fully closed.
Threat model: Ortega-Fernandez, Kowalczyk, Warr (2026); Rinberg et al. (2025)
Team REIGN · 2

## Slide 3
02 · WHY WE CHOSE THIS IDEA
Four reasons
The stakes are high
Model weights are among an AI company’s most valuable assets. Once copied, they cannot be taken back.
It is under-defended
Most AI security work protects the prompt side. Few tools watch the server that runs the model.
The science is new and solid
Published 8 Oct 2026, accepted as an oral at a NeurIPS 2026 workshop, with a formal proof.
It can be reproduced
Open models, a public dataset and every formula are in the paper. No official code exists yet.
Team REIGN · 3

## Slide 4
03 · THE RESEARCH
“Anytime-valid detection of LLM weight exfiltration”
I. Ortega-Fernandez, M. Kowalczyk, K. Warr — MATS Research, NASK, Anthropic · arXiv:2610.11843 · NeurIPS 2026 Workshop “E-Values: From Statistics to ML” (oral)
Finding (4 models, 1,000 streams of 250 responses) | E-process | Per-token alarm
Seed-blind attack detected | 100% | 0%
Median responses to alarm | 6–14 | —
Honest streams falsely alarmed | 0% | ≈100%
False-alarm guarantee over time | ≤ 1% | none
All figures from the paper (Table 1). Models: Llama-3.2-3B, OLMoE-1B-7B, Qwen3-32B, Qwen3-30B-A3B. Prompts: LMSYS-Chat-1M.
Team REIGN · 4

## Slide 5
04 · THE KEY INSIGHT
It is not whether a token differs on replay — it is where it differs.
41–87%
of honest responses already contain a replay mismatch, caused by GPU numerical noise. Counting mismatches alone is useless.
< 0.1%
benign mismatch rate at wide seeded margins, versus 10–40% at near-ties. A wide-margin mismatch is hard to explain by noise.
Source: arXiv:2610.11843, Appendix A, Table 2 and Figure 2
Team REIGN · 5

## Slide 6
05 · PROPOSED SOLUTION
How VILLE works
Step | Stage | What happens
1 | Serve | Production server answers with a committed sampling seed (Gumbel–Max)
2 | Replay | Trusted verifier recomputes the token the seed prescribes at every position
3 | Measure | Record each mismatch and its seeded margin; build 7 nested margin events
4 | Calibrate | On trusted benign traffic, bound each event’s rate (Clopper–Pearson)
5 | Accumulate | After each response, update the e-process: evidence grows only on sustained excess
6 | Alert | Evidence ≥ 200 → incident raised for the security team
Method as specified in arXiv:2610.11843, Section 2 and Appendix B (α = γ = 0.005, c = 0.5)
Team REIGN · 6

## Slide 7
06 · INNOVATION & UNIQUENESS
Check after every response, forever — and the chance of ever raising a false alarm stays below 1%.
— Combines weak evidence across many responses instead of judging single tokens
— No threshold is tuned on attack data — seven margin levels are averaged
— Guarantee proven via Ville’s inequality; holds however long monitoring runs
Team REIGN · 7

## Slide 8
07 · WHAT TEAM REIGN ADDS
The paper gives the detector. We turn it into a defence system.
1 · Drop-in sidecar
Packaged monitor that sits next to any inference server, with SIEM-ready alerts and an audit log.
2 · Calibration-drift guard
The paper’s guarantee needs calibration to transfer. We detect prompt or serving-stack drift and trigger recalibration automatically.
3 · Respond, not just detect
As evidence rises, automatically withhold logprobs and tighten rate limits — the attacker’s decoder depends on them.
4 · One view of both sides
Server-side VILLE plus prompt-side garak scans and NeMo Guardrails in a single SOC dashboard, with Nemotron-written incident summaries.
Items 1–4 are our proposals; the detector and its guarantee are the paper’s.
Team REIGN · 8

## Slide 9
08 · PROPOSED TECHNOLOGY STACK
Open source end to end
Component | Purpose
NVIDIA Nemotron (open weights) | The model being protected; drafts plain-language incident reports
TensorRT-LLM or vLLM | Production inference server with seeded sampling
Hugging Face Transformers | Independent trusted verifier for replay
Python, NumPy, SciPy | E-process monitor and calibration
NVIDIA garak, NeMo Guardrails | Prompt-side testing and protection, complementing VILLE
Reproduction targets the paper’s setup first: bfloat16, temperature 1, top-k 50, top-p 0.95, ≤ 512 output tokens
Team REIGN · 9

## Slide 10
09 · FEASIBILITY & KNOWN LIMITS
What the paper says it cannot yet do
Slow, seed-aware attackers
Attacks sending a few hundredths of a bit per token can go undetected within 250 responses.
Noisier model stacks
Both mixture-of-experts models showed 3–4× more benign mismatches, giving attackers more cover.
Calibration must transfer
The guarantee assumes the same prompts, model, hardware and serving stack as calibration.
Small secrets still escape
Low rates slow bulk weight theft, but do not stop leaking short secrets such as keys.
Team REIGN · 10

## Slide 11
10 · FUTURE SCOPE & IMPACT
Our plan
1. Reproduce the paper’s results on Llama-3.2-3B with open code (our implementation).
2. Extend to an e-process on the continuous fixed-seed score — the paper’s stated future work — to catch slower attackers.
3. Ship our additions: sidecar, drift guard, automatic response and the unified SOC view.
References (VILLE is independent, unofficial work based on these)
Ortega-Fernandez, Kowalczyk, Warr — Anytime-valid detection of LLM weight exfiltration, arXiv:2610.11843 (2026)
Rinberg et al. — Verifying LLM inference to detect model weight exfiltration, arXiv:2511.02620 (2025)
Karvonen et al. — DiFR: Inference verification despite nondeterminism, arXiv:2511.20621 (2025)
Team REIGN · Chittimilla Saitarun · SaiNithin Pokala · github.com/Nithyon/ville